WALES TOWNSHIP

1372 Wales Center Road

Wales, MI 48027

(810) 325-1517     fax:(810) 325-9009

E-mail:  wales@walestownship.org

Building Inspector:  Jim Waddy  (810) 650 1714

Electrical Inspector: Paul Raicevich (586) 873-2660

Mechanical & Plumbing Inspector: Tim Kelly (810) 392-2582

## RE: Electrical Information

A site plan is required to show the location and height of the electric meter on all additions, remodeling projects, and decks.

Detroit Edison requires meters to be a minimum of 3 ½ feet above decking.

ARC FAULT protection is required on all bedroom circuits.

An electrical permit may be necessary in order to move the electrical meter.

*****************

NOTICE: Michigan Electrical Code 250.52 (A) (3) requires that reinforcing rods or bars located in concrete footings be boded to the electrical system. An electrical permit must be secured and an electrical inspection approved prior to placement of concrete. FAILURE TO DO SO MAY RESULT IN A REQUIREMENT TO DISMANTLE PORTIONS OF THE FOUNDATION OR FOOTING.

******************

According to Detroit Edison: Overhead services are no longer allowed when installing for the first time or upgrading.

When installing a New service it MUST be underground.

When upgrading an EXISTING OVERHEAD service it MUST be changed to an underground service.

Please call the Detroit Edison Planner or the Township Electrical Inspector with any questions or concerns. These are major changes and you may want to avoid any costly mistake ahead of time.

*******************

If you have any questions, please feel free to call the office